BASIC SOAP RECIPE

Materials by weight:

Olive oil – 75oz (2.13 kg)

Vegetable Shortening or Crisco – 50 oz (1.42 kg)

Lye – 16 oz (454 g)

Ice water – 45.72 oz (1.3 kg)

Optional Material:

Powdered oatmeal – 12 oz (340g)

Fragrance (Lavender oil or other scents desired)

Procedure:

- Weigh lye and water. Put water in a container with a pouring spout (e.g. pplastic water pitcher)

- Add lye to water slowly. DO THIS OUTSIDE OR IN AN AREA WITH VERY GOOD VENTILATION. BE CAREFUL YOU DO NOT GET THIS ON YOUR HANDS OR IN YOUR EYES.

- Weigh out vegetable shortening and melt over low hat stirring frequently. When melted, add olive oil.

- Let temperature of oil cool to ~110oF (43oC)

- Pour steady stream of lye in to oil stirring constantly. Use electric “stick – blender”.

- Continue stirring until the mixture thickens .

- Add oatmeal powder and fragrance to mixture and stir until evenly distributed with a wooden spoon.

- Pour soap mixture into plastic molds that have lined with plastic cling film. A container with cover is the best.

- Leave the soap at least for 24 hours. It should be hardened (fully saponified) and ready for cutting into bars. Dry the soap bars for at least a month before you use them.