##### AM-466 Final Project

#### Winter 2005

Thermal Transport

of

Steady Fluids Flow

## Student	:	Yosua Jabby Setyobudhi

Student ID :	250126738

## Supervisor : 	Dr. Weijiu Liu

Faculty of Science

The University of Western Ontario

23 pages

SUMMARY

This final project is to demonstrate the advantage of using Finite Element Method to formulate and solve complex problem involving coupled partial differential equation. Moreover, it is to make a simulation of thermal energy transport of non-viscous and incompressible fluids flow in a pipe which is one of many applications in two-dimensional boundary value problems.

INTRODUCTION

First of all, I would like to thank my supervisor Dr. Weijiu Liu who has been very helpful throughout the course and the project. The passion and effort that he has shown in teaching the course has motivated me to for the knowledge of Finite Element Method and its application to formulate and solve complex problems in many different areas of studies. FEM is one of the most powerful methods in giving approximation of complex problems in areas including biology, mathematical finance, medical image, engineering, etc. It is made even easier with the main codes provided so that every user would only have to worry about the INCLUDE files concerning mostly about the boundary conditions and coefficients of the problem.

PROBLEM

figure 1

The illustration shows fluid entering on the left with a uniform velocity and temperature which flows around the pipe which produces energy per surface area of the pipe per unit time. Furthermore, by the assumption of non-viscous and incompressible fluids, the flow is unaffected by the temperature field and thus there is no coupling between the fluid flow and the temperature field.

MESH GENERATION

MESH of the problem could be generated in many different ways with their own advantages. Basically the more we break the MESH into pieces, the more accurate of a solution that we will get, but then also there will be more of computation cost when the MESH is too complicated.

The dimension of the MESH of the problem is given with the diameter of the pipe to be 7.5 units of length with the region area of 20 units by 50 units. The circular are in the center represents the pipe and should not be included in the MESH as it is not affected by the fluid flow and temperature of the dimension.

MESH which I propose consists of six elements, where each element would be broken into more quadrilateral elements.

figure 2

Elements’ sides are specified as follow

figure 3

The six elements then connected with each other by specifying the coincide sides of the elements. Further more, it forms MESH with 140 elements, 168 nodal points with 4 nodes per elements.

The next step is to minimize the bandwidth required for the mesh we just created. Because of the difficulty of finding the true minimum bandwidth required, then one strategy that we use is by trials to obtain at least a decent/acceptable bandwidth.

This new node numbering is specified by using nodes 5 and 15 as the first wave.

Result:

-----------------------------------------

Bandwidth

-----------------------------------------

IB  =    20

Symmetric:     Bandwith =  DOF*IB

NonSymmetric:  Bandwith =  2*DOF*IB-1

DOF = degrees of freedom per node

-----------------------------------------

figure 4

FLOW OF IDEAL FLUIDS

Let Ux and Uy by the x and y components of velocity respectively, then

- Incompressible flow is given by the condition:   ∂/∂x  Ux   +   ∂/∂y  Uy  = 0

To satisfy the condition, we introduce potential function ψ so that

Ux = ∂ψ/∂y    and Uy = - ∂ψ/∂x

- Irrotational fluid is given by the condition: 	∂/∂y  Ux   -   ∂/∂x  Uy  = 0

Then to satisfy the condition, we substitute in the potential function to obtain:

∂ 2ψ        ∂ 2ψ

--------   +   --------   = 0, which we recognize as the Poisson equation in two dimensions.

∂ x2	   ∂ y2

FLOW ANALYSIS

The velocity field is given by:

Ux  =  x-component of velocity  =  ∂ψ/∂y

Uy  =  y-component of velocity  =  - ∂ψ/∂x

Where ψ is the solution of the Poisson equation: 	∂ 2ψ            ∂ 2ψ

--------     +     --------    = 0

∂ x2	        ∂ y2

Therefore, by solving the Poisson equation as stated above using suitable boundary condition, we can obtain the x and y components of velocity that would be needed to specify the thermal transportation.

For the boundary condition, it would depend on the geometry of the MESH:

TOP side:		ψ = 10

BOTTOM side:	ψ = -10

LEFT side:		ψ = y-coordinate

RIGHT side:		ψ = y-coordinate

CIRCULAR area:	ψ = 0.0

Then by steady.m we solve to obtain:

figure 5

TEMPERATURE ANALYSIS

For the sake of simplicity of the project, lets assume that

k = thermal conductivity of the fluid	 = 1

ρCp = heat capacity of the fluid	 = 1

Then the temperature field is given by the equation:

∂/∂x ( k ∂Φ/∂x ) + ∂/∂y ( k ∂Φ/∂y ) -  ρCp Ux ∂Φ/∂x - ρCp Uy ∂Φ/∂y = 0.0

where Ux and Uy is obtained from the flow analysis.

Boundary condition:

TOP side:		q = 0.0

BOTTOM side:	q = 0.0

LEFT side:		Φ = 0.0

RIGHT side:		q = 0.0

CIRCULAR area:	q = 1.0

Coefficient:

For all elements, we have to calculate the velocity components as

Ux =  ∂ψ/∂y    = [DNDY] {VP}

Uy = - ∂ψ/∂x  = [-DNDX] {VP}

Where Ux and Uy is the sum of all the derivative of the shape function of the 4 nodes on the current element and VP as the solution of the low field.

Thus, the coefficient of  ∂Φ/∂x and  ∂Φ/∂y are  -ρCp Ux and ρCp Uy respectively where ρCp = 1

By solving VP at different entrance velocity (0, 0.3, 0.6, and 1) we obtain different temperature field which shows how the temperature is affected by the fluid flow at different velocity level.

SOLUTION

V = 0										          figure 6

V = 0.3									          figure 7

V = 0.6									          figure 8

V = 1.0									          figure 9

V = 1.5									         figure 10

CONCLUSION

As we see that from the problem above, non-viscous and incompressible fluid flow affects the thermal condition in the MESH; it shows the interaction between flow field and the temperature field resulting thermal transportation at different velocity level. Finite Element Method is used in this problem to make such a complicated problem to be easier and can be solved in several simple steps. Improvements can be done where we can obtain more accuracy by increasing the number of elements in the MESH, and do more trials to obtain new nodes numbering which leads to better bandwidth in order to increase efficiency. Another improvement would be to solve for non-ideal fluid condition which would mimic more into the real world problem. In conclusion, FEM makes the job easier to approximate solutions on problems involving high order partial differential equations on complicated boundary value problem.

MATLAB INPUT CODES for STEADY.m

MESH

JOIN

%     JOIN ARRAY

0 0   0 0   0 0   0 0

1 2   0 0   0 0   0 0

0 0   2 3   0 0   0 0

0 0   1 4   0 0   0 0

4 4   0 0   0 0   0 0

0 0   3 4   0 0   5 3

LOOPS

%-----------------------

%     NUMLPS    NNPE

%-----------------------

6       4

%-----------------------

%     NDIV-1    NDIV-2

%-----------------------

4         5

5         6

4         5

4         5

5         6

4         5

COORD

%     LOOP Coordinates (8 per loop)

%----------------------------------------------1

-25        0

-25        -5

-25        -10

-13.825825 -6.325825

-2.65165   -2.65165

-3.46455   -1.43506

-3.75      0

-14.375    0

%----------------------------------------------2

-2.65165   -2.65165

-13.825825 -6.325825

-25        -10

0          -10

25         -10

13.825825  -6.325825

2.65165    -2.65165

0          -3.75

%----------------------------------------------3

3.75         0

3.46455    -1.43506

2.65165    -2.65165

13.825825  -6.325825

25         -10

25         -5

25         0

14.375     0

%----------------------------------------------4

-25        10

-25        5

-25        0

-14.375    0

-3.75      0

-3.46455   1.43506

-2.65165   2.65165

-13.825825 6.325825

%----------------------------------------------5

-25        10

-13.825825 6.325825

-2.65165   2.65165

0          3.75

2.65165    2.65165

13.825825  6.325825

25         10

0          10

%----------------------------------------------6

2.65165    2.65165

3.46455    1.43506

3.75       0

14.375     0

25         0

25         5

25         10

13.825825  6.325825

NPCODE.m

%---------------------------------

% NPCODE.m

%

% A user INCLUDE code

%

% LNP(I,J,K) = node K, on side J

% of element I.

%-------------------------------------

% --------------------------------

% Set n-factor for number of nodes

% on a side

% --------------------------------

if NNPE == 6 | NNPE == 8

n=2;

else

n=1;

end

% ------------------------

% Initialize NPcode array

% ------------------------

for i=1:NUMNP

NPcode(i)=0;

end

%  ---------------------------------

%  Set NPcode = 1 on left boundary

%  ---------------------------------

IEND = n*NDIV(1,1)+1;

for I=1:IEND

NI=LNP(1,1,I);

NPcode(NI)=1;

end

IEND = n*NDIV(4,1)+1;

for I=1:IEND

NI=LNP(4,1,I);

NPcode(NI)=1;

end

%  ---------------------------------

%  Set NPcode = 3 on right boundary

%  ---------------------------------

IEND = n*NDIV(3,3)+1;

for I=1:IEND

NI=LNP(3,3,I);

NPcode(NI)=3;

end

IEND = n*NDIV(6,3)+1;

for I=1:IEND

NI=LNP(6,3,I);

NPcode(NI)=3;

end

%  -----------------------------------

%  Set NPcode = 2 on bottom side of mesh

%  -----------------------------------

IEND = n*NDIV(2,2)+1;

for I=1:IEND

NI=LNP(2,2,I);

NPcode(NI)=2;

end

%  ------------------------------------

%  Set NPcode = 4 on top side of mesh

%  ------------------------------------

IEND = n*NDIV(5,4)+1;

for I=1:IEND

NI=LNP(5,4,I);

NPcode(NI)=4;

end

%  ------------------------------------

%  Set NPcode = 5 on inner circle of mesh

%  ------------------------------------

IEND = n*NDIV(1,3)+1;

for I=1:IEND

NI=LNP(1,3,I);

NPcode(NI)=5;

end

IEND = n*NDIV(2,4)+1;

for I=1:IEND

NI=LNP(2,4,I);

NPcode(NI)=5;

end

IEND = n*NDIV(3,1)+1;

for I=1:IEND

NI=LNP(3,1,I);

NPcode(NI)=5;

end

IEND = n*NDIV(4,3)+1;

for I=1:IEND

NI=LNP(4,3,I);

NPcode(NI)=5;

end

IEND = n*NDIV(5,2)+1;

for I=1:IEND

NI=LNP(5,2,I);

NPcode(NI)=5;

end

IEND = n*NDIV(6,1)+1;

for I=1:IEND

NI=LNP(6,1,I);

NPcode(NI)=5;

end

NEWNUM

Inputs are: MESHo, NODES, NP (all produced from MESH)

Output: NWLD

FLOW

COEF

%------------------------------------------------------*

%                                                      *

%   d    d@    d    d@      d@     d@                  *

%   --(RX--) + --(RY--) + BX-- + BY-- + G@ + HV = 0    *

%   dx   dx    dy   dy      dx     dy                  *

%                                                      *

%------------------------------------------------------*

RXJ = 1;

RYJ = 1;

BXJ=0;

BYJ=0;

GVJ = 0;

HVJ = 0;

INITIAL.m

%-------------------------------

%    INITIAL.m

%

%    Set problem parameters.

%-------------------------------

for Ix=1:NUMNP

%-------------------------------

% Bottom side      --> PHI = -10

%-------------------------------

if NPcode(Ix) == 2

NPBC(Ix)=1;

PHI(Ix)=-10;

%-------------------------------

% Top side          --> PHI = 10

%-------------------------------

elseif NPcode(Ix) == 4

NPBC(Ix)=1;

PHI(Ix)=10;

%-------------------------------

% Circular area      --> PHI = 0

%-------------------------------

elseif NPcode(Ix) == 5

NPBC(Ix)=1;

PHI(Ix)=0;

%-------------------------------

% Left side          --> PHI = y

%-------------------------------

elseif NPcode(Ix) == 3

NPBC(Ix)=1;

PHI(Ix)=YORD(Ix);

%-------------------------------

% Right side         --> PHI = y

%-------------------------------

elseif NPcode(Ix) == 1

NPBC(Ix)=1;

PHI(Ix)=YORD(Ix);

else

NPBC(Ix)=0;

end

end

NEWPHI

%input: PHI

%output: VP

%    newPHI = velocity * PHI

%    this example shows VP at velocity of 0.6

load PHI     -ASCII

newPHI = 0.6*PHI;

save VP newPHI -ASCII

TEMP

COEF

%------------------------------------------------------*

%                                                      *

%   d    d@    d    d@      d@     d@                  *

%   --(RX--) + --(RY--) + BX-- + BY-- + G@ + HV = 0    *

%   dx   dx    dy   dy      dx     dy                  *

%                                                      *

%------------------------------------------------------*

RXJ = 1;

RYJ = 1;

%Initialize Ux and Uy ( velocity components )

Ux = 0;

Uy = 0;

for i=1:NNPE

TEMPi = VP(NP(I, i));

Ux = Ux + DNDY(i)*TEMPi;

Uy = Uy - DNDX(i)*TEMPi;

end

% PCp = heat capacity = 1

BXJ= (-1)*(1)*Ux;

BYJ= (-1)*(1)*Uy;

GVJ = 0;

HVJ = 0;

INITIAL.m

%-------------------------------

%    INITIAL.m

%

%    Set problem parameters.

%-------------------------------

load VP     -ASCII

for Ix=1:NUMNP

%-------------------------------

% NPCode 2, 4, 5     --> q = 1.0

%-------------------------------

if NPcode(Ix) == 2

NPBC(Ix)=0;

Q(Ix)=0.0;

elseif NPcode(Ix) == 4

NPBC(Ix)=0;

Q(Ix)=0.0;

elseif NPcode(Ix) == 5

NPBC(Ix)=0;

Q(Ix)=1.0;

%-------------------------------

% NPCode 3           --> q = 0.0

%-------------------------------

elseif NPcode(Ix) == 3

NPBC(Ix)=0;

Q(Ix)=0.0;

%-------------------------------

% NPCode 3           --> q = 0.0

%-------------------------------

elseif NPcode(Ix) == 1

NPBC(Ix)=1;

PHI(Ix)=0.0;

end

end

List of Codes

Code             Description                                                                       Page

- JOIIN		MESH-JOIN     ______________________________    13

- LOOPS	MESH-LOOPS       ___________________________    13

- COORD	MESH-COORD     ____________________________   13-14

- NPCode	MESH-NPCode     ____________________________   14-16

- COEF		FLOW-COEF     _____________________________    17

- INITIAL.m	FLOW-INITIAL.m      _________________________    17-18

- Newphi	FLOW-Newphi     _____________________________   18

- COEF		TEMP-COEF     ______________________________    19

- INITIAL.m	TEMP-INITIAL.m     __________________________    19-20

List of Figures

Figure             Description                                                                       Page

- Figure 1	Problem illustration     _________________________    3

- Figure 2	MESH elements       __________________________     4

- Figure 3	Elements sides     _____________________________    4

- Figure 4	New node numbering     ________________________   5

- Figure 5	Streamline plot     _____________________________    7

- Figure 6	Temperature field at V = 0     ____________________    9

- Figure 7	Temperature field at V = 0.3     ___________________   9

- Figure 8	Temperature field at V = 0.6     __________________    10

- Figure 9	Temperature field at V = 1.0     __________________    10

- Figure 10	Temperature field at V = 1.5     __________________   11

Bibliography

- Erick G. Thompson,Introduction To The Finite Element Method. John Wiley & Sons, Inc, 2005.

- Harlow, Essex. The Mathematical methods in fluid dynamics. Longman Scientific & Technical ; New York : Wiley, 1993.